## Slide 1
UNDERGRADUATE THESIS PROPOSAL
CSE 4100: Project or Thesis with Seminar Part I
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR
Varendra University
Department of Computer Science and Engineering
7th Semester | Section E
Presenters
Abdul Momit Talukder — 232311320
Oishi Farzana — 232311294
Mahfuz Ahmad — 232311307
SUPERVISOR
Mohd Ruhul Ameen
Lecturer
Department of CSE
Varendra University

## Slide 2
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
2 / 16
How Do Machines “See” 3D?
Distance + Direction → 3D Geometry
Room
Measure
Rays
Rotate
Points
Reconstruct
Point cloud
Notes: Abdul. Keep this intuitive: a sensor measures distance, we know which direction it was pointing, and together that gives one 3D point. Rotate the sensor and repeat, and the points build up into the geometry of the room.

## Slide 3
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
3 / 16
3D Sensing Is Powerful — But Expensive
$500+
Commercial LiDAR
~$25
Our target
High performance is expensive.
Low cost often means lower accuracy.
Notes: Abdul. Commercial LiDAR starts around $500+; our target for the whole scanner is roughly $25. The tension: low cost usually costs accuracy. This thesis is about closing that gap with the sensor's own signal information.

## Slide 4
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
4 / 16
Why Time-of-Flight?
Ultrasonic
Wide beam
Lower spatial resolution
Radar
Strong indoor complexity
ToF
Compact
Fast
Fine spatial sensing
SELECTED
Notes: Abdul. Keep it light. Ultrasonic has a wide beam and lower spatial resolution; radar brings strong indoor complexity. Time-of-flight is compact, fast, and gives fine spatial sensing, so that is what we chose.

## Slide 5
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
5 / 16
Our Hardware Architecture
Proposed final platform
VL53L1X ToF Sensor
Pan–Tilt Mechanism
ESP32
SUPPORTING SENSORS
MPU6050 IMU
DHT11 Temperature
INA219 Power monitor
ACTUATION
DC Gear Motor — Pan
N20 Motor — Tilt
TB6612FNG — Motor driver
Notes: Abdul (team leader, hardware lead). Walk the diagram: VL53L1X ToF sensor on a pan-tilt mechanism, driven by a DC gear motor (pan) and an N20 motor (tilt) through a TB6612FNG driver, all coordinated by the ESP32. MPU6050, DHT11 (temperature, an auxiliary feature) and INA219 support the system. Explain why this architecture was chosen and that this is the PROPOSED final platform, not the pilot prototype.

## Slide 6
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
6 / 16
From Concept to Pilot
Preliminary SG90-based prototype used for pilot data collection
68,000+
pilot measurements
2 indoor campaigns
Pilot prototype ≠ Final thesis platform
Notes: Abdul. This is what we actually built and tested: an SG90-based pan-tilt prototype that produced 68,000+ measurements across two indoor campaigns. Explain how it was assembled and what we learned, and why it motivates optimizing the hardware for the final thesis. Important: this prototype is NOT the final proposed platform. (Replace the placeholder with the photograph from the proposal.)

## Slide 7
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
7 / 16
Scan → Measure → Repeat → Reconstruct
Pan
Tilt
Measure
Point
Repeat
A few points
Hundreds of points
Thousands of points
Each distance measurement becomes one 3D point.
Notes: Oishi. No equations. The scanner turns, takes a distance reading, and records one point; repeat that thousands of times and the points form a 3D picture of the room.

## Slide 8
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
8 / 16
The Real World Is Messy
ToF
Weak Return
Mixed Returns
Ambient Noise
→ Range Error
Notes: Oishi. Real rooms are messy. A dark surface sends back a weak return; reflective or mixed surfaces send back mixed returns; bright room lighting adds ambient noise. All of these show up as range error. Keep it non-technical.

## Slide 9
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
9 / 16
Scale the Evidence
Indoor
Outdoor
Different Lighting
Different Surfaces
PROPOSED TARGET
150,000+
measurements
Paired with ground-truth measurements
Notes: Oishi. The pilot gave 68,000+ measurements; the final thesis proposes 150,000+ (a target, not yet achieved) across indoor and outdoor environments, different lighting and different surfaces, each paired with ground truth. More varied data is what lets a model handle new rooms.

## Slide 10
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
10 / 16
Will It Work in a New Environment?
DARK ROOM
Model works
NEW / BRIGHT ROOM
Error increases
NEW ENVIRONMENT
?
Can it generalize?
Open challenge for the final thesis — not yet solved.
Notes: Oishi. A model can look good in the room it learned from, then lose accuracy somewhere new or brighter. Whether it carries over to a completely new environment is the open question this thesis is designed to test. We have NOT solved it yet.

## Slide 11
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
11 / 16
Democratizing 3D Sensing
Education
Affordable research
Robotics
Low-cost spatial awareness
Assistive Technology
Obstacle/environment sensing
Advanced sensing should not require expensive hardware.
Notes: Oishi. Who benefits: education and affordable research, robotics needing low-cost spatial awareness, and assistive technology for obstacle and environment sensing. Keep it inspirational but grounded: we are not claiming a finished product.

## Slide 12
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
12 / 16
Don’t Use Distance Alone
Raw Distance
Pan Angle
Tilt Angle
Signal Rate
photon-related telemetry
Ambient Rate
photon-related telemetry
Temperature
auxiliary · DHT11
Signal-Aware ML
Predicted Error
Corrected Distance
Signal rate + ambient rate: the sensor’s own internal signal information
Notes: Mahfuz. The idea: do not trust raw distance alone. Feed the model raw distance, pan and tilt angle, plus VL53L1X signal rate and ambient rate (internal photon-related telemetry) and DHT11 temperature (an auxiliary environmental feature, not photon telemetry). The model predicts the range error (residual formulation), which is then used to produce a corrected distance. Signal rate and ambient rate are the core signal-aware contribution.

## Slide 13
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
13 / 16
From Python to ESP32
Train
Python / ML
Transpile
Model → C
Deploy
ESP32
< 100 μs
inference target
Zero external runtime dependency
Notes: Mahfuz. Train in Python, transpile the trained model to C, and deploy on the ESP32 so inference runs on the device with no cloud or external runtime. < 100 μs is an inference TARGET. In the pilot we completed preliminary ESP32 model transpilation; final model selection and deployment are proposed thesis work.

## Slide 14
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
14 / 16
Pilot Results: Promising, but Not Final
94.7%
MAE reduction
Day 2 pilot
22.4 mm
MAE
pooled pilot training
Chart: Relative MAE, Day 2 pilot (raw = 100%)
| Raw | Calibrated
Relative error | 100 | 5.3
PILOT · PRELIMINARY
Not a final accuracy guarantee
XGBoost: 49.34 mm MAE (Day 2 pilot)
Pilot results; final evaluation will use corrected ground truth and scan-level validation.
Notes: Mahfuz. Pilot only. In the Day 2 pilot, XGBoost reached 49.34 mm MAE, a 94.7% MAE reduction; pooled pilot training reached 22.41 mm MAE under the current pilot protocol. The bar chart shows relative error derived from the 94.7% reduction (raw = 100%, calibrated = 5.3%). These are NOT final thesis performance: the final evaluation will use corrected, object-aware ground truth and scan-level / leave-one-scan-out validation.

## Slide 15
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
15 / 16
From Pilot → Robust System
1
Optimize Hardware
Compare pan-tilt actuator options
2
150K+ Measurements
Indoor + outdoor, improved ground truth
3
Third Unseen Environment
Held-out test of generalization
4
Prove Generalization
Scan-level, leave-one-scan-out validation
Final 3D reconstruction + ESP32 deployment
Notes: Mahfuz. Four stages, simplified from the proposal timeline: optimize the hardware, collect 150K+ measurements, test on a third unseen environment, then rigorously validate generalization with scan-level / leave-one-scan-out validation. The end goal is a final 3D reconstruction with the selected calibration model deployed on the ESP32.

## Slide 16
Signal-Aware ML Calibration for Low-Cost Pan-Tilt LiDAR · Thesis Proposal
16 / 16
Built to Be Shared
CODE
GitHub
HARDWARE
Open design
DATA
Public dataset
Low-cost sensing. Reproducible research. Open access.
https://github.com/Mr-Mahfuz/signal-aware-tof-calibration
Thank You
Questions?
Notes: Mahfuz. Close on openness: code on GitHub, open hardware design, and a public dataset. Then thank the committee and invite questions. Central idea to repeat: we are turning a very cheap ToF sensor into a more capable 3D sensing system by using the sensor's own signal information to learn and correct its errors directly on the edge.

## Slide 17
Test Title